## Slide 1: MetaPhys: Few-Shot Adaptation for Non-Contact Physiological Measurement
Xin Liu et.al / 2021
채종의 & 문종현
May / 19 / 2023

## Slide 2: CONTENTS
Introduction
Model-Agnostic Meta-Learning (MAML)
Methods
Experiments
Result & Discussion

## Slide 3: Introduction
rPPG(remote Photoplethysmography)
  RGB 카메라를 이용하여 반사광 피부변화를 감지하는 비접촉 생체신호 추출 기술
  Sequence to Sequence / Signal Reconstruction

## Slide 4: Introduction
생체 신호(맥박, 호흡, 혈압 등)의 생리학적 특성 또는 외부 환경 요인에 의해 개인차
Personalization/fine-tuning의 필요성 : 기존의 ML 모델은 새로운 Subject (Task)에 대해 일반화/편향 이슈를 가짐.
Personalized Model: 소수의 데이터를 통해 일반화/편향 이슈를 개선하고, 새로운 Task에 대해서도 빠르게 적응/조정.
Unsupervised learning의 필요성 : Oximeters와 같은 Contact sensor의 경우, 언제 어디서든 휴대/사용할 수 없으며
기기 자체의 미세조정이 요구됨. 즉, True Label (PPG signal)없이도 얼굴 영상 데이터만으로도 PPG를 예측할 수 있어야 함.
Label Generator: 얼굴 영상 기반 unsupervised physiological measurement (e.g. POS)를 통해 Pseudo Label을 생성).
개인의 생리학적 특성
1) 나이 2) 성별 3) 피부색 4) 체중 5) 신장
외부 환경 요인
1) 측정 장비 (Oximeter & Camera) 2) 조명 종류 및 밝기
rPPG 신호 측정에 영향을 주는 요인

## Slide 5: Introduction(cont.)
UBFC Dataset (Mostly Caucasian)
MMPD Dataset (African / Asian)

## Slide 6: Introduction(cont.)
Challenge of Supervised Learning in this task
Camera-based sensing
  Environmental differences: Intensity & Composition of the incident light.
  Camera sensor differences: Auto adjustments or Video codec...
  Individual differences: Appearance (skin type, facial hair...) & Physiology (pulse dynamics..)
  Contextual differences: Motions in the Videos
Data Collection & Acquisition
  Requires advanced technical expertise (Handling of Sensor/Device)
  Identity of the subjects & sensitive health information (Privacy)
 그래서 적은 샘플로 일반화 성능을 달성해야 하며, 또는 Pseudo Label를 생성하여 학습해야 필요가 있음.

## Slide 7: Introduction(cont.)
Major Contribution
Meta-learning Framework for camera-based Vital Sign measurement
Cross-dataset Evaluation compared to other method
Test sensitivity during adaptation(fine-tuning)
Performance Analysis for subjects with different skin types

## Slide 8: Model-Agnostic Meta-Learning (MAML)
Meta Learning  Learning to Learn
 적은 양의 샘플을 갖는 새로운 Task에 대해서도 빠르게 학습/적응할 수 있도록 모델을 학습하는 방식.
…
Task1
Task2
MAML
Fine-Tuning
Optimal Point
for new tasks
Key Assumption
Maximizing the sensitivity of the loss functions of new tasks with respect to the parameters.
 새로운 task에 대한 작은 변화에도 해당 task의 손실함수를 크게 변하게 하는 모델 파라미터가 있다.
Pretraining
 MAML produces a general initialization as the starting point for fast adaptation to a diverse set of unseen tasks.

## Slide 9: MAML(cont.)
Figure 0. model-agnostic meta-learning algorithm (MAML)
각각의 task()가 적은 수의 gradient update만으로도 각자의 optimal parameter()로 빠르게 수렴/적응할 수 있는 모델()을 학습하는 알고리즘.
여기서, : parametrized function with parameters θ
Inner-loop (Update using Support set)
Outer-loop (Update using Query set)
MetaPhys case...
0) Pretrained Backbone  TS-CAN(using AFRL dataset)
1) Task  Subject (Each Video = Support + Query Set)
2) Support & Query Set  Split the video frames
3) Loss Function  Mean Squared Error (MSE)

## Slide 10: MAML(cont.)
Global Minima for each Dataset
UBFC Dataset
MMPD Dataset
UBFC Dataset
MMPD Dataset

## Slide 11: MAML(cont.)
Optimal Point for Fast Adaptation with New task

## Slide 12: Method – Physiological Meta-Learning
Algorithm for MetaPhys : Unsupervised adaptation with unlabed data

## Slide 13: Method – Physiological Meta-Learning(cont.)
Spatial and Temporal Model Architecture Backbone (TS-CAN)
 Temporal 정보를 추출하는 Motion Branch와 Spatial 정보를 추출하는 Appearance Branch로 구성.
Motion Branch : Normalized Difference Frames의 시간에 따른 움직임(즉, 피부색의 변화)을 추출하여 PPG Signal을 추정.
Appearance Branch : 이미지 시퀀스의 Averaged Frame으로 부터 ROI (피부 중 이마, 광대) 영역에 대한 Attention Mask를 생성.

## Slide 14: Method – Physiological Meta-Learning(cont.)
Plane Orthogonal-to-Skin (POS)
 얼굴 영상의 피부색 변화(RGB)를 기반으로 HR과 관련된 신호를 추출하는 Pseudo Label Generator 역할을 수행.
Implementation Procedure
1) Spatially averaging pixel values for each frame with the region-of-interest. (ROI selection & Averaging)
2) Temporally normalizing the resulting signals within a certain window size calculated relative to the frame rate. (Normalization)
3) Applying a fixed matrix projection to offset the specular reflections and other noise. (POS)
4) Bandpass filtering of the resulting pulse waveform. (Filtering)

## Slide 15: Method – Physiological Meta-Learning(cont.)
𝜃
𝜃 : Pre-trained model
G : POS for pseudo labels
: Support frames from
: Query frames from
: Model trained with Support Set
: Gradients with Query Set
: Optimal model for Fast Adaptation
Query Set
Dividing Support and Query Set
Updating the personal params
Updating the global params for fast adaptation
𝜃
Pretraining TS-CAN

## Slide 16: Experiment
Dataset composition
Pretraining Dataset : AFRL
Cross-dataset Training & Evaluation : UBFC <-> MMSE
Support set & Query set
For each individual(or Task or Subject) from 30 fps video
Size of the Support set : 540 video frames(=18 seconds)
Size of the Query set : 360 video frames(=12 seconds)
Other Implementation Details
Sample Sequence Length : 10 frames(baseline)  20 frames(modified)
Inner-loop : SGD optimizer with an inner learning rate(α) of 0.005
Outer-loop : Adam optimizer with an outer learning rate (𝛽) of 0.001
Training 10 epochs (MAML)  One step adaptation (Fine-tunning)

## Slide 17: Result & Discussion
Supervised & Unsupervised MetaPhys(with pretraining)이 전반적으로 우수한 성능을 보임.
Pretraining을 하지 않은 MetaPhys (No pretrain)의 경우, 제안한 방법(MetaPhys with pretraining)보다 성능이 떨어짐.
Pseudo Label Generator로 사용된 Unsupervised POS method 보다 성능이 좋아짐.

## Slide 18: Result & Discussion(cont.)
Visualizing Adaption – Attention Mask generated from Appearance Branch

## Slide 19: Result & Discussion(cont.)
Robustness to Skin Type
 Limitation : 그래도 여전히 어두운 피부색에 대한 편향 문제는 존재

## Slide 20: Implementation
Inner Loop
https://wandb.ai/paperchae/rppg/workspace?workspace=user-paperchae
https://github.com/remotebiosensing/rppg/blob/jh_main/rppg/configs/FIT_METAPHYS_MMPD.yaml
Chart: Training Time according to Inner Update
| 1 | 2 | 3 | 4 | 5
time (sec) | 20 | 34 | 49 | 65 | 78

## Slide 21: Implementation(cont.)
Outer Loop
https://wandb.ai/paperchae/rppg/workspace?workspace=user-paperchae

## Slide 22: Unsolved Problems & Possible Solutions
Pretrained model 𝜃
  Using 𝜃 which is trained with the small dataset to overcome the small dataset?
  >> 데이터셋의 분포, 크기를 변경하며 Pretrained-Model에 따른 성능 비교 평가 필요
Train & Test with Same Individual with (Updated global params)
  Overfitted to Individual? Or the Video itself?
  >> Personalization은 하나의 개인의 특성을 잘 배우는 것이 목표라고 생각하면, 한 사람에서 취득한 다양한 환경(같은 사람, 다른 조명 환경)에 대한 데이터에 대한 테스트 필요
POS as Pseudo Label Generator?
  Reliability Issue as Ground Truth
  >> Labeling System을 새로 구축(Video-to-PPG)하여 POS에 대한 Reliability 검증 필요

## Slide 23: Q&A
Keywords : rPPG, Meta-Learning, Vital Datasets
감사합니다.